## Slide 1: Virtual Machines
Benjamin Brewster

## Slide 2: Why You Need to Care
Because someday you’ll have to:
  Use a particular piece of software that only runs on an OS you don’t easily have available
  Deploy a robust, easily-maintainable production environment
  Do something dangerous
  Recover from a horrible, heinous disaster after which 3 people will go to jail except you

## Slide 3: Virtualization
A System Virtual Machine is an emulated instance of an operating system running on a supportive Host
The OS thinks it’s running on hardware, but it’s just accessing software hooks provided to it that appear as hardware
A HDD in a VM is stored as a single file on the Host
Network adapters in the VM transfer data to the Host, which handles the actual network traffic

## Slide 4: Hosts and Guests and Hypervisors
A hypervisor is a program that runs virtual machines
A host machine is the system that runs the hypervisor
The individual virtual machines running on the hypervisor are called guest machines
Host Machine
OS
  nmap
OS
Spreadsheet Program
Calculator
Hypervisor
Guest Machine
OS
  ping
Guest Machine

## Slide 5: Hypervisor Types
Host Machine
OS
  nmap
OS
Spreadsheet Program
Calculator
Hypervisor
Guest Machine
OS
  ping
Guest Machine
Host Machine
OS
  nmap
Hypervisor
Guest Machine
OS
  ping
Guest Machine
Type 1, Bare-metal, Native
Type 2, Hosted

## Slide 6: Why Virtualize?
Makes experimentation and prototyping easy
  No need to get a bunch of hardware: your desktop PC/server can run it all, even multiple VMs all simultaneously
  Set up and teardown is much faster with software than hardware
Increasingly complex applications, running on diverse OSs, can all be easily managed from one place: the supporting Host
Improved security and robustness of the VM/snapshot/hypervisor ecosystem
More easily manage massively large-scale deployment with tremendous efficiency gains as servers are scaled up and down as needed

## Slide 7: Process Virtual Machines
A software machine, easily adaptable to any target host OS, that is able to run applications written in an intermediate language
The “Java Virtual Machine” (JVM) is the most common example
The JVM executable itself has been ported to run on countless operating systems, enabling Java programs to run unchanged anywhere the JVM does
Host Machine
OS
Spreadsheet Program
Calculator
Java: UPS Management Utility
Java: Minecraft
Java: Custom Database GUI

## Slide 8: Full vs. Partial Virtualization
Full Virtualization means that there is enough hardware being simulated by the host that the guest virtual machine can be unmodified - it doesn’t necessarily know that it’s contained as merely a process elsewhere
If you have to modify the guest virtual machine to get it to run, then it is not fully virtualized
Hardware-Assisted Virtualization:
  The hardware doesn’t have to be fully emulated on the host: the host may have actual hardware designed for the guest virtual machines to use

## Slide 9: Origins
Historically, virtual machines grew from time-sharing:
Save PROC A state
Load
PROC B state
PROCESS A
10 ms
PROCESS B
10 ms
Save PROC B state

## Slide 10: Origins
If it works with set of processes, then why not with a process that emulates hardware sufficiently well to run an OS in it?
Save PROC A state
Load
PROC B state
PROCESS A
10 ms
Save PROC B state
Virtual Machine Process

## Slide 11: Configuring VirtualBox
Set the VM folder somewhere useful
File -> Preferences -> General -> Default Machine Folder
Say
Demonstrate

## Slide 12: Creating a CentOS CLI-Only VM Template - 1
Start up VirtualBox
Click the New button
Name it whatever you like
Change Type to Linux, and Version to Other Linux (64-bit)
Set Memory Size to 1024MB
Make sure “Create a virtual hard disk now” is selected
Click Create
Say
Demonstrate

## Slide 13: Creating a CentOS CLI-Only VM Template - 2
Necessary, because otherwise CentOS will think the drive is too small to be installed onto
Pick a location for the VM
Set VHD size to 8GB
Make sure VDI is selected
Select Fixed Size
Click Create
Say
Demonstrate

## Slide 14: Creating a CentOS CLI-Only VM Template - 3
Select the new VM you just created
Click Start (Normal Start)
Select the CentOS7 .iso file for the Start Up Disk
Click Start
Say
Demonstrate

## Slide 15: Creating a CentOS CLI-Only VM Template - 4
The install will do some set up, and then requires a few more things to be checked.
When the machine starts, select Install CentOS Linux 7 and hit Enter
Select English and click Continue
Click NETWORK & HOST NAME
Turn Ethernet on by clicking the toggle button in the upper right
Click Done
Say
Demonstrate

## Slide 16: Creating a CentOS CLI-Only VM Template - 5
Network time prevents you from toggling between AM/PM to and 24-hour time
Click DATE & TIME
Change Timezone by clicking the map itself
Turn Network Time off, if it’s on
Change to AM/PM
Turn Network Time on
Click Done
Click INSTALLATION DESTINATION
Then just click Done
Click Begin Installation
Click ROOT PASSWORD, set something complicated and random, then save it into a file (you won’t be using it much, if ever)
Click Done
Say
Demonstrate

## Slide 17: Creating a CentOS CLI-Only VM Template - 6
Optionally, skip ahead here to the “Fresh Install” snapshot already created
Click USER CREATION
Type Full Name
Pick a username (I recommend you use your ONID username)
Check the “Make this user administrator” box
Type in a real password
Click Done
Click Finish Configuration
When it appears, click Reboot
Say
Demonstrate

## Slide 18: Creating a CentOS CLI-Only VM Template - 7
You could shutdown now with "$ sudo shutdown" to get a truly blank VM, but I like to instead first customize it with my ~/.bashrc file
"." is another way to use the source command
Let it auto-select and boot
At the prompt, login
$ curl http://web.engr.oregonstate.edu/~brewsteb/.bashrc > .mybashrc
$ vi .bash_profile
Add this to the end of the file:
  . ./.mybashrc
Save and exit vi
Say
Demonstrate

## Slide 19: Creating a CentOS CLI-Only VM Template - 8
This enables the stuff in ~/.mybashrc.
More importantly - and this is critical for deploying new systems - it tests your recall/storage of the username & password
Shut the VM down
In Settings, set the VM to use 2 CPUs
Now your VM is ready to be duplicated - don’t use this one again!
The duplicate allows us to have a ready-made starting point if/when our production VM gets borked
Log out and back in
$ sudo halt
Click the X in the corner, select "Power Off The Machine."
Say
Demonstrate

## Slide 20: Creating a CentOS CLI-Only VM Template - 9
CentOSU, Centaur, one of the Hobbit’s Dwarven names, a Tolkien placename, a city name, etc.
Now you’ve got a stable clone to play around with! Make clones like this for whatever CentOS project you’d like.
Right-click on the CentOS Template VM, and click Clone
Type a new name
Check the “Reinitialize MAC address box”
Click Next
Select Full Clone to create a complete 8GB+ duplicate
Select Linked Clone to create a snapshot of the original VM and link the new VM to that state; copying in the future requires both VMs
Click Clone
Start Clone
Say
Demonstrate

## Slide 21: Start Windows VM
Takes a LOT longer to start; we’ll come back to this later
Start up Windows VM
Say
Demonstrate

## Slide 22: Snapshots
A snapshot is a file that contains the current state of a virtual machine, including memory, at a specific moment in time
You can then return to this state, as needed!
Examples for why you’d want to do this:
  To duplicate the VM at this point in time
  To reset a computer lab PC back to a certain point at the end of the day
  As a backup or archive: you can go back and get the contents of the files as of the snapshot, when your “lets try this” idea/virus destroys everything
You can take unlimited snapshots
We can do this easily in VirtualBox, which we’ll play with in the coming slides

## Slide 23: Causing Havoc and Saving the World
Verify you’re in the VB VM!
Start up CentOS Clone
Machine -> Take Shnapshot
$ rm -rf /
$ rm --no-preserve-root -rf /
$ ls
File -> Close
In right pane of VirtualBox, right-click Shnapshot name, then hit Restore
Click Restore
See the restored VM
Say
Demonstrate

## Slide 24: Web Browsing in our Windows VM
Your connections with this web browser will still be tracked back to this Host, since the originating IP address in the next upstream device’s connection logs will be that of this Host
Page requests are all made in plain HTML, since the protocol is text-based
This is a good way to sandbox your browsing so you don’t get infected
Log in and fire up Edge
Say
Demonstrate

## Slide 25: Shared Drag'n'Drop & Clipboard
Drag and drop files
Share whiteboard between the host and guest
Machine -> Settings -> General -> Advanced
Set Shared Clipboard to Bidirectional
Enable Drag’n’Drop to Bidirectional
Show copy/paste and drag'n'drop between Host and Guest VM
Say
Demonstrate

## Slide 26: Install Guest Additions into Guest VM
Installing Guest Additions allows us to:
  Mount a shared folder
  Run in Seamless mode, which just removes the window features
Try Seamless Mode
Get out with RCTRL+L
Devices -> Insert Guest Additions CD Image…
D:\VBoxWindowsAdditions.exe
Click Next a billion times
Reboot the VM when asked
View -> Seamless Mode
Say
Demonstrate

## Slide 27: Mount a Shared Folder
Pick the folder in the Host that will actually hold the data.
The Guest VM will have access to this via a network share.
Map a network drive to this share
Machine -> Settings -> Shared Folders
Click the Add Share button on the right
In Folder Path, choose the path on the Host VM that will actually hold the data. Choose Auto-mount, then give it a name
Click OK
Access the shared folder from the Guest VM by accessing:
  \\vboxsvr\<folder share name>
In Guest VM, open Windows Explorer
Click Map Network Drive up above
Pick drive letter, browse to share, mark "Reconnect at sign-in checkbox", click Finish
Say
Demonstrate

## Slide 28: Start Up MacOS VM
Instructions for making your own image:
  https://www.howtogeek.com/289594/how-to-install-macos-sierra-in-virtualbox-on-windows-10/
Various aspects of this Mac VM will not work, namely TimeMachine, Messages, FaceTime, etc.: things that use the Apple hardware specifically or are otherwise deeply tied to the Apple ecosystem
Fire up VM, log in to “macuser” account
Start Safari and browse the web
Say
Demonstrate

## Slide 29: Conclusion
Virtual Machines are here to stay - get used to spinning them up, then spinning them down as needed
Hypervisor software changes and updates frequently, so stay on top of it
Employers LOVE your VM experience