## Slide 1: Proper LAN Deployment
Benjamin Brewster

## Slide 2: Why You Need to Care
Because someday you’ll have to:
  Design and deploy a network for your business or home
  Understand someone else's broken network so you can fix it
  Automate IT, which requires understanding a typical network

## Slide 3: Networking in the Real World
Network engineers attempt to lay connections across a physical hellscape full of EM, sharp edges, clueless users, hackers, faulty equipment, and lying weasels
You will see awful things
  Like that blue Netgear switch I found connecting everything while immersed in mud, outdoors, under a viewing platform, on a coastal cliff
You will see things that will make you wonder why people haven't been fired, sued, arrested, or defenestrated
  Like that heavily advertised, password-less WIFI network that connected the general public to the main company server at a tourist destination

## Slide 4: An Ideal Network (?)
Networks can be complicated, but they break down into simple graphs like this
Even if the cables are running hundreds of feet from room to room, or across the 3rd floor of the dorm
Note: no loops allowed!
LAN = Local Area Network
WAN = Wide Area Network
These terms are more descriptive than definitional

## Slide 5: An Ideal Network
Let's look at an idealized, practical LAN with one subnet
Routers interpret between two different network subnets
Switches merely connect devices together & ignore subnet restrictions
ROUTER
x0
x1
SWITCH
x0
x1
x2
x3
x4

## Slide 6: An Ideal Network
WAN (wide area network) means outside your LAN
Every WAN interface is contained in a subnet on some other router; to the upstream router, our router is just another device:
ROUTER
x0
x1
SWITCH
x0
x1
x2
x3
x4
WAN
LAN
LAN

## Slide 7: An Ideal Network
Each router interface:
  Must be on a different subnet
  Has an IP address on that subnet
Unmanaged switches do not have IP addresses on any interface: switches gonna switch
CIDR /24 (Class C) subnet 254 Hosts
LAN
CIDR /30 subnet 2 Hosts
WAN
SWITCH
x0
x1
x2
x3
x4
ROUTER
x0
x1

## Slide 8: Getting IP
The LAN-facing interface of a router typically runs a DHCP server in most homes and businesses
The hosts run a DHCP client to get IP addresses on the subnet
Both sides of the router need to have an IP address assigned:
  WAN side can be either dynamic or static
  LAN side is always static so clients can find it
ROUTER
x0
x1
SWITCH
x0
x1
x2
x3
x4
LAN
WAN

## Slide 9: Sample Network Settings
Router interfaces & data:
  Default Gateway: 10.0.2.2
  x0:
    Network: 10.0.2.0/24
    IP: 10.0.2.15
  x1:
    Network: 192.168.1.0/24
    IP: 192.168.1.1
    Runs DHCP server for network, handing out:
      DHCP start: 192.168.1.10
      DHCP end: 192.168.1.240
      Default Gateway: 192.168.1.1
      DNS Server: 192.168.1.1
ROUTER
x0
x1
SWITCH
x0
x1
x2
x3
x4
Gets IP: 192.168.1.10
Also gets default gateway, DNS server

## Slide 10: Our VirtualBox Network Setup
Our virtual network will consist of:
  VirtualBox itself to act as switches and cabling between the hosts
  VMs for the hosts
  A VM host running pfSense as the router
  VirtualBox VirtualBox VirtualBox this software is amazing - we can simulate all the parts of a network!

## Slide 11: pfSense
pfSense is a complete software router that can be installed onto practically any hardware: from IoT-scale, to PCs, to massive purpose-built network devices, like 48-port firewalls
Robust, stable, in active open-source development, fast, easy to deploy and configure, works out of the box
Based on BSD, not Linux
Can use both CLI and web interface to configure

## Slide 12: Our VirtualBox Network Setup - Details
Pay attention! This is used in the Lab!
This is our router, note two interfaces on two different networks
"Attached to" differences:
  NAT: VB issues an IP to the adapter via internal DHCP
  Internal Network is internal only: any VMs can talk on that, but there is no connection to the WAN here
Adapter type specialty: virtio net drivers are optimized for VMs
The CS312LAN Internal Network is our base switch
Boot pfSense_Reference
Boot CentOS_GUI_Reference on CS312Lan Internal Network
Show the VirtualBox main screen
Select "pfSense_Reference"
Settings -> Network
Show all settings on Adapter 1 and 2
Say
Demonstrate

## Slide 13: Our VirtualBox Network Setup - Details
In contrast to our router, see that there's only one interface, and it's on the virtual switch
Select "CentOS_GUI_Reference"
Settings -> Network
Show all settings on Adapter 1 and 2
Say
Demonstrate

## Slide 14: pfSense Booted
Note how there isn't a good way to see detailed settings - you have to do that from the web, unless you're really good with BSD networking commands
We can verify that we have DNS resolution and networking in one step
Ping to test DNS and network
Return to the menu
Getting in and out of pfSense VM using Host Key (RCTRL on Windows)
In pfSense main console menu, see the assigned WAN & LAN addresses
Menu 8 to get to shell
# nslookup www.google.com
# ping www.google.com
# ping 8.8.8.8
# exit
Say
Demonstrate

## Slide 15: CentOS GUI Networking - All DHCP
Talk about IP address, default gateway (called "Default Route"), and primary DNS server
You can see that the information is all set to Automatic via DHCP, so none of this has to be set
However, we can change to a new address! We don't have to stay on this one
In our CentOS GUI VM, click on networking/sound/battery button in upper-right corner, click "Wired Connected", then click "Wired Settings"
Have "Wired" selected on the left
Click gear icon in bottom right
Click IPv4 on left
Say
Demonstrate

## Slide 16: CentOS GUI Networking - Change to Static
However, we can change to a new address! We don't have to stay on this one
Thanks Linux! I'm never giving you to my grandma
THAT has an effect
See that we can still access the web!
Change "Addresses" to Manual
Set:
  IP: 192.168.1.250
  Netmask: 255.255.255.0
  Gateway: 192.168.1.1
  DNS: 8.8.8.8
Hit Apply, note that this has no effect!
$ sudo systemctl restart network.service
Browse teh webz
Say
Demonstrate

## Slide 17: Rescuing a Device Outside the Subnet
Being able to change IP addresses manually like this is handy, because sometimes we need to rescue orphan machines, like this Alpine one
The Alpine VM starts statically at 192.168.2.200. We can't ping this from our CentOS GUI machine, because this is outside the subnet the CentOS GUI machine is on
Start "Alpine_RescueMe" VM
From CentOS GUI:
$ ping 192.168.2.200
Set static IP:
  IP: 192.168.2.250
  Netmask: 255.255.255.0
  Gateway: 192.168.2.1
  DNS: Leave at 8.8.8.8
Hit Apply
$ sudo systemctl restart network.service
$ ping 192.168.2.200
Say
Demonstrate

## Slide 18: Rescuing a Device Outside the Subnet
Now, we can ping it!
Let's connect!
This is where the network configuration is stored
Currently set up as a bogus static assignment
Replace the current one with the dhcp config
This would be setting the assignment however is proper for what you're trying to do
Now we can access the system on the proper subnet!
$ ping 192.168.2.200
$ ssh root@192.168.2.200 (yes, if asked)
  u: root; p: password
$ cd /etc/network
$ ls -pla
Examine the three interfaces files!
$ cp interfaces.bak.dhcp interfaces
$ reboot
Change CentOS back to DHCP IP address
$ sudo systemctl restart network.service
$ ping 192.168.1.19 (or whatever it shows)
Say
Demonstrate

## Slide 19: Playing with pfSense Settings: Admin
Let's connect to our pfSense router's GUI config pages and see what we can find
Connecting to the default gateway's address via HTTP is usually a great way to find the router's config page
The Assignments page shows us the names of the interfaces as pfSense sees them, and how they are assigned.
This page shows a ton of stuff for managing the router itself
Important here is the TCP port, which is occasionally changed to meet some other networking requirement, like a port-forwarding rule
Never fail silently! This just sets the path of communication up - you set up actual alerts elsewhere.
Start Firefox, go to 192.168.1.1
Log in with admin/password
Click on Interfaces -> Assignments
Click on System -> Advanced
Talk about webConfigurator (the router's web page system) section, TCP port field.
Explain Notifications tab usage.
Say
Demonstrate

## Slide 20: Playing with pfSense Settings: Admin
DNS settings and the name of the router can be changed here.
I've also changed the theme to be Dark, since I usually have lights off in my office
Click on System -> General Setup
Say
Demonstrate

## Slide 21: Playing with pfSense Settings: WAN
Here, we can change the WAN interface from getting it's config via DHCP, or whether it's statically assigned; both static and DHCP WAN assignments are common
Click on Interfaces -> WAN
Talk about DHCP Client Configuration section, "Reject leases from" field, and the dorm router story.
Talk about Reserved Networks section, "Block private networks and loopback addresses" field. Handy!
Say
Demonstrate

## Slide 22: Playing with pfSense Settings: LAN
IP config for LAN interface of the router is static so that it can be easily found by devices on the subnet
See how IPv4 Configuration Type is set to "Static IPv4"
Say
Demonstrate

## Slide 23: Playing with pfSense Settings: DHCP
We can configure the DHCP settings here
In pfSense, we can leave the DNS servers fields alone in order to distribute the system default DNS settings. We can override the defaults here.
Similarly, the Default Gateway field can be overridden.
The Domain is for allowing those services that need it to know where they are (normally Windows)
Static ARP makes it so that only the MAC addresses listed below can access the router on this interface, i.e. the ARP table can't be changed.
This sounds good, but MAC addys can be spoofed.
Click Services -> DHCP Server
Show the Range fields
Show and explain DNS, Gateway, and Domain name fields.
Show Static ARP field
Say
Demonstrate

## Slide 24: Playing with pfSense Settings: UPnP
Bonus feature! If you decide to set up pfSense as your router, and you do any gaming, make sure to enable UPnP!
UPnP allows a device to open ports on the router/firewall and configure port-forwarding rules that point to itself, so that external devices can connect automatically
If that sounds like a massive security hole, you're right: it's normally something you only find on routers designed for home use.
It's often not even an option on business-class routers!
Click Services -> UPnP
Say
Demonstrate

## Slide 25: Conclusion
The network terms and settings we normally concern ourselves with are:
  WAN
    Getting an IP and DNS settings for the WAN
  LAN
    Defining the LAN's IP network
    Providing DHCP to that network
pfSense makes some great router software!
We'll be talking about WiFi, VPNs, and Firewalls next time